## Slide 1
ASSC
Automatic Sleep Stage Classification
解正平 劉維凱 張景程

## Slide 2
Outline
Introduction
Data acquisition
Preprocessing
Classification
  XGboost
  Deep neural network
XGB – Feature extraction
  time analysis
  frequency analysis
  time frequency
  Complexity measures
XGB – training
NN – Convolutional neural network
  Architecture
  Model description
NN – training
Classification Result
Application – alarm clock
Mindwave mobile
  ThinkGear protocol
  Package Decode
Android App
  App inventor
  App engine
Reference

## Slide 3
Sleep stage Classification in machine learning
  Non-linear model
  Neural network
EEG feature analysis
Application for alarm clock
Introduction

## Slide 4
EDF [expanded] database
  SC file (20 subjects 40 files)
    Record at home
    2 nights = 40 hours
  ST file (22 subjects 22 files)
    Mild difficult falling asleep
    Record at hospital
    9 hours
EDF browser (.edf -> .csv)
hard to classify together
Data acquisition

## Slide 5
1 epoch = 30s = 30*sampling rate(100Hz) = 3000 data
Remove forward and backward epochs while not sleeping
label in 6 stages [w, s1, s2, s3, s4, R]
label in 5 stages [w, s1, s2, s3, R]
Select [Fpz-Cz] single EEG signal
Preprocessing

## Slide 6
Xgboost
  Feature extraction
  Feature selection
  Training
Neural Network
  Build model
  Training
Classification

## Slide 7
XGboost

## Slide 8
Time analysis
  Standard statistics
Frequency analysis
  Power ratio for delta, theta, low_alpha, high_alpha, beta
Time frequency
  WT analysis
Complex measures
  entropy
99 features 60 hours
XGB – feature extraction

## Slide 9
Petrosian Fractal Dimension
Detrended Fluctuation Analysis
Hurst exponent
Shannon entropy
Spectral entropy
Approximate entropy
Maximum-minimum distance
Energysis
Complexity measures

## Slide 10
Regression tree
6 fold validation, early_stop = 10
Feature selection
Set threshold to retrain
XGB - training

## Slide 11
XGB - accuracy
Validation accuracy = 0.824
Testing accuracy = 0.834
F1 score = 0.760
Sensitivity = 0.834
[w, s1, s2, s3, R]
= [151, 78, 452, 148, 171]

## Slide 12
XGB – plot importance
PFD (86) | Esisen high alpha (97)
DWT mean cA6/cD5 (79) | DWT std cA6 (70)
DWT mean cD4/cD3 (77) | DWT avgPower cA6 (71)
Dwt mean cD5/cD4 (78) | Hurst exponent(88)
Kurt (3) | Skew (2)

## Slide 13
XGB – feature select
Chart: feature select
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
train_acc | 0.6284 | 0.68352 | 0.72029 | 0.75775 | 0.80023 | 0.81323 | 0.84125 | 0.84874 | 0.84949 | 0.88106 | 0.88118 | 0.88752 | 0.87611 | 0.89005 | 0.8906 | 0.90178 | 0.90865 | 0.90893 | 0.91742
train_f1 | 0.49148 | 0.55074 | 0.62058 | 0.67952 | 0.73913 | 0.76116 | 0.79493 | 0.80284 | 0.80616 | 0.8473 | 0.84883 | 0.85708 | 0.83974 | 0.86101 | 0.85809 | 0.87349 | 0.8826 | 0.88416 | 0.89301
test_acc | 0.65061 | 0.67265 | 0.70612 | 0.71184 | 0.76082 | 0.75837 | 0.77061 | 0.81306 | 0.77633 | 0.80816 | 0.80571 | 0.80163 | 0.80163 | 0.81224 | 0.81143 | 0.81714 | 0.82531 | 0.83837 | 0.82694
test_f1 | 0.50153 | 0.53765 | 0.61108 | 0.62509 | 0.66707 | 0.6672 | 0.69807 | 0.73288 | 0.70517 | 0.73633 | 0.73878 | 0.73519 | 0.72108 | 0.73789 | 0.74531 | 0.73982 | 0.76026 | 0.76647 | 0.74015
sensitivity | 0.50286 | 0.54785 | 0.60564 | 0.61917 | 0.66049 | 0.66094 | 0.68652 | 0.72268 | 0.6966 | 0.72614 | 0.72815 | 0.72475 | 0.71333 | 0.72755 | 0.7384 | 0.73111 | 0.74899 | 0.76019 | 0.73444
Feature size | Train acc | Train f1 score | Test acc | Test f1 score | sensitivity
18 | 0.9089 | 0.8842 | 0.8384 | 0.7665 | 0.7602
99 | 0.9545 | 0.9411 | 0.8286 | 0.7721 | 0.7659

## Slide 14
Deep Neural Network

## Slide 15
How it works…
Convolutional Neural Network

## Slide 16
CNN - model architecture
64 Conv , 50
64 Conv , 400
30S EEG signal
MaxPool, 8
MaxPool, 4
128 Conv , 8
128 Conv , 6
128 Conv , 8
128 Conv , 6
128 Conv , 8
128 Conv , 6
MaxPool, 4
MaxPool, 2
Fully Connected, 1024
FC , 5
out

## Slide 17
CNN – input raw data

## Slide 18
Utilizes two CNNs with different filter sizes at the first layers.
  - Extract features from raw single-channel EEG.
Small filter : capture temporal information (certain EEG pattern)
Large filter : capture frequency information
CNN – model description

## Slide 19
Learning Curve
Testing accuracy : 0.86 (1720/2000)

## Slide 20
CNN – confusion matrix

## Slide 21
Application

## Slide 22
Wake up in a comfortable mood
Moitor sleep quality
App connect to Internet
Application – alarm clock

## Slide 23
Get EEG raw data
AAA battery
Bluetooth
Mindwave mobile

## Slide 24
Value introduction
Package structure
Command bytes
Mindwave – ThinkGear protocol

## Slide 25
header and payload
Mindwave – package decode

## Slide 26
Alarm at a specified time
Alarm in a specified time interval
Get value from cloud drive
Android App

## Slide 27
Sexagesimal
am. and pm.
App – App inventor

## Slide 28
Special treatment at 11 pm. to 01 am.
App – App inventor

## Slide 29
Google app engine
A Server to enable inventor access
App – App engine

## Slide 30
Reference
[1] Alickovic, Emina, and Abdulhamit Subasi. "Ensemble SVM method for automatic sleep stage classification." IEEE Trans. on Instrumentation and Measurement (2018).
[2] Nakamura, Takashi, et al. "Complexity science for sleep stage classification from EEG." Neural Networks (IJCNN), 2017 International Joint Conference on. IEEE, 2017.
[3] Ebrahimi, Farideh, et al. "Automatic sleep stage classification based on EEG signals by using neural networks and wavelet packet coefficients." Engineering in Medicine and Biology Society, 2008. EMBS 2008. 30th Annual International Conference of the IEEE. IEEE, 2008.
[4] Aboalayon, Khald Ali I., et al. "Sleep stage classification using EEG signal analysis: a comprehensive survey and new investigation." Entropy 18.9 (2016): 272.
[5] Yulita, Intan Nurma, Mohamad Ivan Fanany, and Aniati Murni Arymurthy. "Combining Deep Belief Networks and Bidirectional Long Short-Term Memory." Proceeding of the Electrical Engineering Computer Science and Informatics 4 (2017): 88-93.
[6] Chambon, Stanislas, et al. "A deep learning architecture for temporal sleep stage classification using multivariate and multimodal time series." arXiv preprint arXiv:1707.03321 (2017).
[7] Zhang, Junming, and Yan Wu. "A New Method for Automatic Sleep Stage Classification." IEEE transactions on biomedical circuits and systems 11.5 (2017): 1097-1110.